## Slide 1: P.A. COLLEGE OF ENGINEERING DEPARTMENT OF COMPUTER SCIENCE & ENGINEERING
SynCura: Predictive ICU Monitoring System Using Attention-Based LSTM
Real-time in-hospital mortality risk with SHAP + temporal-attention explainability
UNDER THE GUIDANCE OF TEAM MEMBERS
Divya K
Abdul Ahad Ikkeri - 4PA24CS002
Fathima Reeha - 4PA24CS026
Fizan Feroz - 4PA24CS032

## Slide 2
P.A. COLLEGE OF ENGINEERING
DEPARTMENT OF COMPUTER SCIENCE & ENGINEERING
ABSTRACT
ICU deterioration is a leading cause of preventable in-hospital mortality; static scores like NEWS2 miss temporal trends.
SynCura uses an attention-based LSTM on 12 features x 90-minute windows with FastAPI backend and React dashboard.
Trained and evaluated on PhysioNet 2012 Challenge data with in-hospital mortality labels (4,000 stays).
Deployed 3-model ensemble (e12+e13+c53): validation AUC 0.840, fresh unseen holdout AUC 0.834.
Provides real-time risk scoring with SHAP and attention explainability; research prototype, not a medical device.

## Slide 3
P.A. COLLEGE OF ENGINEERING
DEPARTMENT OF COMPUTER SCIENCE & ENGINEERING
INTRODUCTION
ICU mortality ranges 10-29%; early detection of deterioration significantly improves outcomes.
Current practice relies on NEWS2, SOFA and APACHE-II with static thresholds and manual calculation.
These scores fail to capture temporal trends and have limited sensitivity for early warning.
Objective 1-2: build attention-LSTM mortality-risk model with full-stack FastAPI and React system.
Objective 3-5: add SHAP + attention explainability, compare against NEWS2, enable scenario simulation.

## Slide 4
P.A. COLLEGE OF ENGINEERING
DEPARTMENT OF COMPUTER SCIENCE & ENGINEERING
LITERATURE SURVEY
Title | Author Names | Year | Features | Limitations
Dynamic real-time ICU risk, longitudinal irregular data | Zheng Z et al. | 2025 | Vitals, labs, meds (EMR) | Retrospective; inflates near discharge; cross-hospital drop
DL in-hospital mortality, long-term sequential ICU data | Yan Z et al. | 2026 | ICD sequences + temporal clinical data | Modest AUC; stacking complexity; external < internal
Multimodal ICU deterioration (time-series + notes) | Sadanandan B | 2026 | Physio time-series + ClinicalBERT notes | Privacy/compute/delay; low AUPRC; untested live
Vital signs for real-time ICU mortality risk | Wu Y et al. | 2024 | BP, HR, RR, Temp (vitals only) | Diff cohort; limited explanation; no deployment
Deep learning to attend to risk in ICU | Nguyen M et al. | 2017 | PhysioNet 2012 + temporal attention | Legacy; limited external validation
RealMIP: real-time risk, continuous data recovery | Xie P et al. | 2025 | Generative recovery of missing vitals | Needs multi-hospital data; heavy model
Deep Interpretable Early Warning (DEWS) | Choi E et al. | 2020 | Hospital vitals; BiLSTM + attention | Retrospective; attention not cause; weak alarms
Attention residual LSTM-FCN (ARLF) | Li Y et al. | 2025 | Clinical time series (LSTM-FCN) | Complex model; limited external validation
Graph attention for in-hospital deterioration | Do T-C et al. | 2023 | Clinical variables as graph | Graph focus; not temporal; alternative angle
Wearable DL in-hospital deterioration | Scheid M R et al. | 2025 | Continuous wearable vitals | Sensor noise/dropouts; irregular sampling
3

## Slide 5
P.A. COLLEGE OF ENGINEERING
DEPARTMENT OF COMPUTER SCIENCE & ENGINEERING
PROBLEM STATEMENT
ICU patients need continuous risk assessment, but bedside scores such as NEWS2, SOFA and APACHE-II depend on single-timepoint thresholds and manual calculation, ignoring vital-sign trajectories, which results in late detection, alarm fatigue and limited sensitivity for early deterioration.
What is needed is an automated model that learns temporal patterns from streaming vitals and labs, and produces interpretable output so clinicians can see which vitals and timepoints drove the risk.

## Slide 6
P.A. COLLEGE OF ENGINEERING
DEPARTMENT OF COMPUTER SCIENCE & ENGINEERING
PROPOSED METHODOLOGY
Dataset: PhysioNet 2012 Challenge, 4,000 ICU stays, 37 variables over 48 hours, mortality labels.
Features (12): HR, RespRate, Temp, SysBP, DiasBP, SpO2 (via SaO2) + GCS, BUN, Creatinine, WBC, Platelets, Glucose.
Preprocessing: 90-min sliding windows, causal per-window interpolation, train-only z-score, patient-level 80/20 split.
Model: 2-layer LSTM-96 with additive temporal attention, BatchNorm, dropout 0.3, weighted BCE, Adam with step decay.
Training: full set-a plus 80% set-b, early stopping on val AUC; 3-model logit-averaged ensemble for deployment.
System: Vitals to FastAPI /ingest to SQLite to ensemble scorer (0-100) to React dashboard and Discord/Telegram alerts.
5

## Slide 7
P.A. COLLEGE OF ENGINEERING
DEPARTMENT OF COMPUTER SCIENCE & ENGINEERING
WORK DONE
Deployed 3-model AttentionLSTM ensemble (e12+e13+c53, 12 features x 90-min window) for in-hospital mortality risk prediction.
Validation AUC 0.840; fresh unseen 20% set-B holdout AUC 0.834 (95% CI 0.825-0.843); one-time locked slices 0.828 / 0.818.
Operating point 0.70 gives precision approx. 0.50 at recall approx. 0.48 (holdout sensitivity 80.3%, specificity 75.2%).
FastAPI backend live: /ingest real-time scoring, /patients ranking, /patient/{id}/explain with SHAP and temporal attention.
React dashboard live: ranked risk board, 5 scenario simulations, threshold tuner with NEWS2 comparison, alert stream.
Explainability verified: SpO2, respiratory rate and systolic BP rank as top drivers; causal interpolation with no future leakage.
6

## Slide 8
P.A. COLLEGE OF ENGINEERING
DEPARTMENT OF COMPUTER SCIENCE & ENGINEERING
FUTURE ROADMAP
Prospective validation, calibration reporting and clinician review before any clinical use (research prototype only).
Migrate training to MIMIC-IV / eICU for larger modern cohort with fairness and subgroup analysis.
Upgrade to Temporal Fusion Transformer for longer histories and improved temporal modeling.
Multimodal fusion: integrate clinical notes with BioBERT alongside vitals and labs.
Federated learning across hospitals with TinyML edge deployment for privacy-preserving monitoring.
Mistake-driven retraining loop: queue confirmed misses and false alarms into weighted retraining with fresh-holdout gating.
7

## Slide 9: REFERENCES
[1] Z. Zheng et al., "Development and Validation of a Dynamic Real-Time Risk Prediction Model for ICU Patients," J. Med. Internet Res., vol. 27, e69293, 2025. (Base paper)
[2] T. I. Alshwaheen et al., "Novel Framework of Patient Deterioration Prediction in ICU Based on LSTM-RNN," IEEE Access, vol. 9, 2021.
[3] E. Choi et al., "Deep Interpretable Early Warning System for Detection of Clinical Deterioration," IEEE J. Biomed. Health Informat., vol. 24, no. 9, 2020.
[4] Y. Li et al., "Attention Residual LSTM-FCN for Inpatient Mortality Prediction," IEEE Access, vol. 13, 2025.
[5] PULSE-ICU: Pretrained Unified Long-Sequence Encoder for Multi-task ICU Prediction, arXiv:2511.22199, 2025.
[6] GARLIC: Graph Attention-based Relational Learning of Multivariate Time Series in ICU, arXiv:2608.10969, 2026.
[7] Z. Yan et al., "Deep learning-based in-hospital mortality prediction using long-term sequential ICU data," PeerJ, vol. 14, e21631, 2026.
[8] M. R. Scheid et al., "Clinical wearable deep learning based continuous deterioration prediction," Nature Commun., vol. 16, 9513, 2025.
[9] PhysioNet/Computing in Cardiology Challenge 2012: Predicting Mortality of ICU Patients (4,000 stays, 37 variables).
[10] L. Wang et al., "Expert Augmented Prediction of Circulatory and Respiratory Instability," npj Digit. Med., 2026.
2026-27
8

## Slide 10: THANK YOU